ESP32 CONFIGURATION STEPS
1. IDE Arduino installation:
Download and install IDE Arduino from official site: https://www.arduino.cc/en/software.

2. Adding ESP32 Support in the Arduino IDE:
- Open the Arduino IDE and go to File > Preferences.
- In the "Additional Boards Manager URLs" section, add the following URL for ESP32: https://dl.espressif.com/dl/package_esp32_index.json
- Go to Tools > Board > Boards Manager....
- Search for "ESP32" and install "esp32 by Espressif Systems".

2.1 Configure the IDE for ESP-EYE:
- Connect the ESP-EYE board to the computer using a USB cable.
- Go to Tools and configure the following:
  - Board: Select ESP32 Wrover Module (it is compatible with ESP-EYE as it uses the same chip).
  - Flash Frequency: 40MHz.
  - Partition Scheme: Select Huge APP (3MB No OTA) (required for applications that use a lot of memory).
  - Port: Select the COM port assigned to the ESP-EYE board.
  - Upload Speed: Set to 115200 (standard for ESP32).

3. Selecting the ESP32 Board:
- Go to Tools > Board and select ESP32 Dev Module (or a compatible ESP32 board).
- Go to Tools > Port and select the COM port to which the ESP-EYE is connected.

4. Connecting and Configuring the ESP-EYE:
Connect your ESP-EYE board to the PC via USB cable.
If the port doesn't appear, try disconnecting and reconnecting the cable, or update the USB drivers for ESP32.

5. Checking the Serial Connection:
- Open the Serial Monitor in the Arduino IDE (Tools > Serial Monitor).
- Ensure that the baud rate of the serial monitor is set to 115200 baud.
- Upload a simple sketch like the following to verify that the ESP32 is working properly:

If the serial monitor displays the message "ESP32 is connected!", it means the communication was successfully established.

6. Uploading the Sketch to ESP-EYE:
- Once the connection is verified, you can upload your code via Tools > Upload.
- After the upload is complete, the ESP32 will start executing the uploaded code.

ISSUES ENCOUNTERED 05/12/2024:
It was not detecting the COM port. It was necessary to update the CP210 driver. The connection was successfully established, and the board connected to the home Wi-Fi. I’m attaching the base code for Wi-Fi connection (testConn.c).