ESP32 KEY FEATURES
The ESP32 is a versatile microcontroller with many integrated features, making it suitable for a wide range of applications, from IoT to signal processing. Here’s a list of its main capabilities:
1. Connectivity
- Wi-Fi
  - Protocol: IEEE 802.11 b/g/n (2.4 GHz)
  - Modes: Access Point (AP), Station (STA), or both (AP+STA)
  - Support for HTTPS and TLS for secure connections
  - Mesh networks with the ESP-MESH protocol
- Bluetooth
  - Bluetooth Classic (for audio and serial communication)
  - Bluetooth Low Energy (BLE) (for IoT applications and low-power devices)

2. Processing Capabilities
- Processor
  - Dual-core or single-core Xtensa LX6 (up to 240 MHz)
  - Multitasking support with the FreeRTOS operating system
- Memory
  - Internal RAM: 520 KB (SRAM)
  - External Flash: from 4 MB to 16 MB (depending on the model)
- Hardware Acceleration
  - AES, SHA, RSA, ECC encryption for security.
  - DSP, (Digital Signal Processing) for audio or sensor applications

3. GPIO (General Purpose Input/Output)
Up to 34 configurable GPIO pins, which can be used as:
- Input
- Output
- PWM (Pulse Width Modulation) for controlling LEDs, motors, etc
- Hardware interrupts
- Analog I/O (ADC/DAC)

4. Communication
- UART: up to 3 serial channels
- I2C: for communication with sensors and devices
- SPI: for high-speed communication with displays, memory, etc
- I2S: for audio applications
- CAN Bus: for industrial or automotive communications
- Ethernet: supported via an external PHY

5. Sensors and Analog Inputs
- ADC (Analog-to-Digital Converter): 12-bit with up to 18 channels
- DAC (Digital-to-Analog Converter): 8-bit with 2 channels
- Hall Sensor: integrated to detect magnetic fields
- Capacitive Touch: up to 10 channels for capacities touch detection (useful for touch buttons)

6. Control
- PWM: Up to 16 channels for controlling motors, LEDs, etc
- Hardware Timers: High precision for generating accurate timings
- Servo Motor: Control via PWM

7. Power and Consumption
- Low Power Consumption:
  - Deep Sleep Mode: Consumes only a few microamperes
  - Light Sleep Mode: Consumes a few milliwatts
- Power Supply:
  - Voltage range: 2.2V – 3.6V
  - Integrated battery management via PMU (Power Management Unit)

8. Software Features
- Operating System: Integrated FreeRTOS for multitasking
- Networking Libraries: Support for HTTP, MQTT, WebSocket, and other IoT libraries
- OTA (Over-the-Air): Remote firmware updates
- Support for MicroPython and Arduino IDE: Easy programming with high-level languages
- Native support for Espressif IoT Development Framework (ESP-IDF): A powerful framework for advanced developers

9. Debugging and Diagnostics
- Serial Monitor: Debugging through USB or UART ports
- Trace and Profiling: Tools for optimizing code performance
- GPIO Debugging: Debugging via signals on configured pins

10. Other Features
- Neural Network and Machine Learning: Support for libraries such as TensorFlow Lite Micro
- Camera Interface: Compatible with modules like OV2640 (ESP32-CAM)
- Display Interface: Support for OLED, LCD, and TFT displays via SPI/I2C